## Slide 1
NAWT OWTS Inspection Standards
Notes: 1
Welcome to the NAWT OWTS Inspection Standards- Inspecting Onsite Wastewater Treatment Systems (OWTS)
Each Trainer Introduces self if you have not done so to this point.
Give your background - Pumper - Installer - SEO - Home Inspector
Housekeeping & Ground Rules – This is an informal Session
Ask questions as you think of them. The greatest resource in this room is you, the trainees. If I get stumped, I’ll count on one of you for the answer!
Pit stops as needed - tell them where toilets are
Cell Phones and pagers on silent or vibrate – If you need to take a call – leave the room…please!

## Slide 2
AGENDA
DAY 1
8:00 AM Introduction (Section 1)
8:30 AM Septic Systems: Components & Equipment (Section 2)
9:30 AM BREAK
10:00 AM Inspector’s Toolbox (Section 3)
12:00 LUNCH
1:00 PM Inspector’s Toolbox (Section 3)
1:30 PM Inspection Procedures (Section 4)
2:30 PM BREAK
3:00 PM Inspection Procedures (Section 4)& Q+A
5:00 PM DINNER (included)
6:00 PM Drawing & Reporting Conclusions (Section 5) (required)
8:00 PM ADJOURN
DAY 2
7:30 AM PREVIEW OF FIELD TRIP
8:00 AM FIELD TRIP
12:45 PM LUNCH
1:30 PM REVIEW FIELD INSPECTIONS & DISCUSSION
2:15 PM CERTIFICATION EXAM
Notes: 2
Review agenda – NEED TO ADJUST AGENDA AFTER PRESENTATIONS HAVE BEEN UPDATED – REMOVE TIMES
2-days - MUST attend both days
first day - all classroom, mid-morning and afternoon breaks
second day- AM meet in classroom; prepare for field sites in the field
lunch
discussion
exam

## Slide 3
Notes: 3
NAWT OVERVIEW
ASK: Raise your hand if you had heard of NAWT before registering for
this course.
NAWT is an organization of septic system professionals;
members include:
State Associations
Pumpers
Installers
Maintenance Providers
System Inspectors
Portable Toilet Providers
System Designers
Anyone interested in or working in the OWTS Industry

## Slide 4
Training Partners
Notes: 4
INTRODUCE
NAWT & CPOW
NOF Research & Education Foundation
NO members
National scope & stature
Nonprofit corporation capable of receiving tax deductible gifts
Third party standards certification endorsement
(click once) Our Training Partners
(click once) And PSMA collaboration of the inspection standards
If you have not already done so - INTRODUCTIONS AROUND
I would like each of you to introduce yourself, home county & current connection to onlot systems, and tell us one thing that is unusual about you . . .
(used to be a gymnastics instructor)
(have a pilot’s license)
(race car driver)

## Slide 5: Program Goals
You Will:
  Learn the administrative foundation for the Inspection Program.
  Review various types of onsite wastewater treatment systems; their components and function.
  Develop the tools needed to properly inspect each of these systems.
  Learn how to conduct a field inspection.
  Learn how to draw and report conclusions.
Notes: NAWT’s GOALS
Enable you to recognize all common OWTS in use ( covered on day one)
Present a systematic approach to identifying all components
Present data gathering techniques
Help you to understand the data gathered
Enable you to reach conclusions regarding the system
Learn how to communicate your findings
Assure inspection process and results are consistent
ASK: What specific goals do you have for this course?
WRITE: Answers on Flip Chart, tape pages to wall in full view; as subject is covered, check off. Before each break revisit list; check off as needed before exam, be sure ALL have been covered
Please get out your materials packet
WORK THROUGH TRAINEE PACK - EXPLAIN EACH PIECE ** If doing a live class you could use the flip chart – zoom may be different
Hold each up as you mention it
Inspection Standards (in binder) Your Field Guide and Desk Resource for conducting inspections
Preliminary Information Form, Field Observation Report Form, Pump Out Report Form
Reference Materials
ASK: Any Questions???

## Slide 6
Notes: 6
THE NAWT STANDARDS
HOLD UP THE INSPECTION STANDARDS
This document is formatted to facilitate inspections. This document “flows” from structure to absorption system - i.e., DOWNSTREAM.

## Slide 7
OPEN YOUR BOOK
TO THE
Table of Contents
Notes: SAY: We want you to understand how the STANDARDS themselves are formatted
The Table of contents should HELP WITH THIS

## Slide 8: UNDERSTANDING THE STANDARDS
Information in black boxes is of
critical importance.
Preliminary Info – A – pages 64-65
APPENDIX
FIELD INSPECTION CHECKLIST- A pages 69-75
Notes: - Understanding how the standards are formatted.
Say: Information in black boxes is of critical importance.
Hold up preliminary information and field forms – Encourage them to follow along in their standards book
(click) SAY: This form is found in APPENDIX A pages 64 & 65 of the standards
Trainer Explains form.
(click) SAY: This forms are found in APPENDIX A pages 69-75 of the standards
Trainer Explains form.
These forms are used in conjunction with the standards.
Each provides space to document some aspect of the system under inspection. The combined data yields a comprehensive picture of the system. They are an important record, which you should maintain indefinitely. They are an excellent defense, should you ever need one. As we move through the discussion, you will see how every piece of information comes into play.

## Slide 9: STANDARD’S RESTRICTIONS
Use of these Standards is restricted to persons who have successfully completed the NAWT sanctioned training associated with these Standards.
Once trained, inspectors are required to complete a refresher course or participate in a continuing education cycle.
Notes: Read the following:
Use of these Standards is restricted to persons who have successfully completed the NAWT sanctioned training associated with these Standards. Once trained, inspectors are required to complete a refresher course or participate in a continuing education cycle ( Min. – Every 2 years).

## Slide 10: WHY???
Why have a set of standards?
Why is consistency important?
Notes: Why have a set of Standards?
LOOKING FOR: So, every inspection is done the same way.
Why is consistency important?
LOOKING FOR: So that when 2 people inspect the same system they reach the same conclusion...every time.
The inspection leads to a report.
This report provides information about the type and condition of the system and provides
suggestions for additional testing or corrective actions that may be needed.

## Slide 11: Your Inspection Goals
Provide Maximum Amount of Information.
Describe the current system.
Enable the CLIENT To draw conclusions.
Notes: YOUR INSPECTION GOAL: to provide the client with as much information about the system as possible so that the client can draw informed conclusions.
In this document these processes are referred to as a “NAWT Inspection.”

## Slide 12: An Inspection is:
Objective
Evaluation & description of all components
Presents conclusions regarding the system:
  Acceptable
  Acceptable w/Concerns
  Unacceptable
  More Investigation is Necessary
Notes: A NAWT OWTS Inspection is:
Objective – your only interest in the system at the time of inspection is a comprehensive inspection.
A description of every component in the system.
A conclusion about the components and system.
Includes a report that communicates the conclusions to the client in a manner that enables an understanding of the findings.
Report is written in clear, easy to understand language.
ASK: Can you send the client a copy of the Field Observations Form as the final report?
LOOKING FOR: NO!

## Slide 13: An Inspection Is Not
A warranty or guarantee
An assurance that there is or will be adequate effluent treatment.
Notes: A NAWT OWTS Inspection is not:
A warranty or guarantee.
It is not an assurance that there is or will be adequate effluent treatment.
STRESS: It is essential that these concepts be clearly stated in every report that is issued.

## Slide 14: Regulatory Requirements
Inspectors are encouraged to become familiar with the regulatory requirements in their service territories.
Notes: This document does not include references to jurisdictional regulations.
You are not doing a regulatory inspection.
Particular state dimensions are used for illustrative purposes.
In the various examples cited, CO regulations are used to illustrate dimensions, capacities and similar characteristics. Where precise dimensions, capacities and characteristics are stated, the inspector should consult the prevailing regulatory standards in the jurisdiction.

## Slide 15: Unusual Systems
Inspectors will encounter components, systems or site conditions that are not specifically described in these Standards.
STRANGE
Notes: Inspectors will encounter components, systems or site conditions that are not specifically described in these Standards.
In all cases, professional judgment consistent with the information provided herein and the goal of determining if the component is performing as intended should be the underlying principles employed by the inspector. When such conditions are encountered, they should be reported to the NAWT office to enable future Standards revisions address those items.

## Slide 16: What Will We Cover?
Inspector Qualifications.
Inspector Training.
How onsite wastewater treatment systems work.
Authorization to inspect.
Gathering preliminary information.
Field procedures.
Making Conclusions.
Inspection reports.
Hydraulic Load Testing.
Resources.
Notes: Over the next two days we will cover . . .
Inspector Qualifications
Inspector Training
How OWTS systems work
Authorization to inspect
Gathering preliminary information
Field procedures
Inspection reports
Hydraulic load testing
Resources

## Slide 17
L
I
E
C
R
OCATE
_ _ _ _ _
_ _ _ _ _ _ _
DENTIFY
_ _ _ _ _ _ _
VALUATE
ONCLUDE
_ _ _ _ _ _ _
EPORT
__ _ _ _ _
Notes: 17
Your primary tasks…(click twice to show blank lines in first row)
ASK Who can fill in the blanks
LOCATE (click once to show answer then again to show next blank line – repeat for all)
IDENTIFY –EVALUATE- CONCLUDE- REPORT

## Slide 18: Qualifications:
If you perform NAWT inspections or sign an inspection report, you MUST …
  Pass NAWT OWTS Inspection training course within the last 2 years or be in the continuing education cycle.
Note: If the above does not apply you cannot use the Standards.
Notes: Before performing a NAWT OWTS inspection or issuing (signing) an inspection report, you must be a currently-certified NAWT inspector.
Training Required for Inspectors.
Complete NAWT OWTS Training Course (minimum requirement), Field instruction (would like to add this back to the curriculum), Score at least 70% on the post-course exam
Trainees and their employers must sign an acknowledgment
Advanced training - CE Cycle
ASK: What is the question every NAWT inspection must answer?
LOOKING FOR: Does the installed system and each component function as intended?
ASK: ANY QUESTIONS
If it was covered, go over it...If it will be covered, say “we’ll get to it.”

## Slide 19: Review Questions Part 1
PART 1 SUMMARY Verbal Exchange
Notes: PART ONE SUMMARY
This Summary is designed to be a quick verbal exchange between the trainer and the participants.
Trainees should be instructed to call out the answers, not wait to be called upon.
If no one calls out an answer, the trainer should point to someone and ask for the answer.
If wrong answers are presented, correct them before moving on.

## Slide 20: NAWT’s GOALS are to:
Enable you to recognize all of the common onsite systems
Present a systematic approach to identifying all system components
Present data gathering techniques
Help you to understand the data gathered
Enable you to reach conclusions regarding system performance
Assure inspection process and results are consistent
Notes: Start out doing the first one yourself . . . NAWT’s GOALS are to:
Enable you to recognize all of the common onsite systems.
Present a systematic approach to identifying all system components.
Present data gathering techniques
Help you to understand the data gathered
Enable you to reach conclusions regarding system performance
Assure inspection process and results are consistent
Trainees should be instructed to call out the answers, not wait to be called upon.
If no one calls out an answer, the trainer should point to someone and ask for the answer.
If wrong answers are presented, correct them before moving on.

## Slide 21: What is your inspection goal?
To provide the client with as much information about the system as possible so that the client can draw informed conclusions.
Notes: ASK: What is your inspection goal?
WAIT for Answers from Class-
*CLICK*
Answer: To provide the client with as much information about the system as possible so that
the client can draw informed conclusions.

## Slide 22: What is your end product?
A Report
That does what ?
Notes: ASK: What is your end product – of the inspection?
Wait for it----
Answer- report ...
..Ask-that does what...describes the system, each component and its condition and presents a conclusion regarding the system’s condition
Acceptable
Acceptable with concerns
Unacceptable
More study / investigation needed

## Slide 23
That describes the system, each component, its condition, and presents a conclusion regarding the system’s condition
NAWT conclusions:
  Acceptable
  Acceptable with concerns
  Unacceptable
  More investigation needed
Notes: that does what?
describes the system, each component and its condition and presents a conclusion regarding the system’s condition
Acceptable
Acceptable with concerns
Unacceptable
More study / investigation needed

## Slide 24: A REPORT IS NOT: WHAT ?
Guarantee
Warranty
Notes: ASK: A REPORT IS NOT A WHAT ?
Guarantee or a warranty

## Slide 25: What are the 4 components of every system?
Source
Initial and Advanced Treatment
Distribution system
Final Treatment / Soil Treatment Area (STA)
Notes: ASK What are the 4 components of every system?
Answer:
Source – Initial and Advanced Treatment – Distribution components/system – Final Treatment / Soil Treatment Area (STA)

## Slide 26: PART 1 Conclusion
QUESTIONS?