## Slide 1: Aquaponics Filtration
©2025 Matt Recsetar

## Slide 2: What is the point of filtration?
Water from the fish tanks is filtered so it can be reused
Elevated suspended solids stressful to fish
High ammonia and nitrite are toxic to fish
Fish waste that isn’t removed increases BOD in fish tanks which lowers DO and degrades water quality
Hydroponic component allows for added filtration and removal of nitrate, lowers overall water usage
  BOD (Biochemical Oxygen Demand) – Amount of DO used by aerobic microbes to decompose organic matter (fish poop)

## Slide 3: Step 1: Solids Removal
Settleable Solids
Mass of solids settled after 1 hour
Total Suspended Solids
Particles > 2 µm or more specifically
Mass of solid particles that can be removed by a GF/C Filter
    Glass microfiber filter – 1.2 µm pore size
1 human cell is about 8 microns

## Slide 4: Removing Settleable Solids (Gravity)
Settling Basins or Sedimentation Basins
Deep cone Clarifiers
Radial Flow Clarifiers
Swirl Separators
From Aquaculture Alliance
From Dura-Tech
From Getchemready.com
Fish poop settles at 3.7-9.2 cm/s (1.5-3.7in/s

## Slide 5: Settling Basins or Sedimentation Basins
*Septic tank

## Slide 6: Deep Cone Clarifiers

## Slide 7: Swirl Separators
Strong horizontal mixing; Weak axial mixing
Sized based on flow rate (Q) and desired solids removal efficiency
Fairly easy to build and a lot of how to videos online. Water leaves from top of a center pipe.

## Slide 8: Radial Flow Settlers (Clarifiers)
Used in wastewater treatment plants
Water enters in the center of the tank and moves ‘radially’ outward
As water slowly moves towards the outer edge, solids fall to the bottom
The weir around the edge keeps floating scum from leaving the tank

## Slide 10: Radial Flow Clarifiers in Aquaculture

## Slide 11: Radial Flow Settlers (clarifiers)
Can purchase conical bottom tanks online from various plastic tank suppliers
If upward water velocity is slower than 1.5 cm/s, you will get good settling

## Slide 12: Removing TSS (total suspended solids)
Granular media filters
  Bead Filters
Microscreen filters
  Rotary Drum Filters
Polygeyser
Bubble Bead Filter

## Slide 13: Floating Bead Filters
Best solids removal mechanism for aquaponics
Remove solids down to about 30 microns
Range from $500 ~ $4000 depending on desired capacity
Sized based on feeding capacity and flow rate

## Slide 14: Bead filter Backwashing Video

## Slide 15: Biofilters
Capture and degrade organic compounds (fish poop)
Nitrification*
Mineralization

## Slide 16: Types of Biofilters
Trickling Biofilters
Rotating Biological Contactors (RBCs)
Submerged Biofilters
Floating Bead Filters
Moving Bed Bioreactors (MBBR)

## Slide 17: Trickling Biofilters
Fixed media bed where water flows (trickles) downward over a thin biofilm on structured or random packed biomedia
Cheap to build
100-300 m3/m2
Good aeration and CO2 stripping (degassing)
TAN removal 0.1-0.9 g/m2
From Ebling

## Slide 18: Rotating Biological Contactors (RBC)
Biodisc filter
100-300 m3/m2
Good aeration and CO2 stripping (degassing)

## Slide 19: Submerged Biofilters
Upflow or downflow (or flow through)
Water flows through biomedia (Gravel, shells, plastic)
Simple and relatively cheap to build
Beneficial for trapping specific contaminants
Can be a good filter for fine solids if needed
  Will require maintenance

## Slide 20
Downflow Biofilters
Typically run on an airlift (or pump)
Water is pushed out from the bottom of the filter causing water to flow down through the biofilter
Upflow Biofilters
Typically run with gravity
Water enters via gravity from above and is inserted at bottom of biofilter and thus pushes water up through biofilter and over its edges

## Slide 21: Moving Bed Biofilm Reactors (MBBR)
Media is kept moving in tank to maximize biofilm use of surface area and maximize scrubbing
Agitators and aeration
Media should occupy 50-70% of container volume
Most common*

## Slide 22: Biofilter Media
Specific surface area – Surface area per unit volume
  More surface area = more room for bacterial growth
Types
  Bioballs
  Kaldness Biofilter media
  Saddle Chips
  Crushed oyster or clam shells
  Gravel
  LECA
Order on Amazon or other online retailers

## Slide 23: Effective Surface Area
Total surface area available for filtration
  Available for bacterial growth
For nitrifying bacteria
Measured in m2/m3 (SA/Volume of media)
  Used to determine filter size and amount of biofilter media needed
Not typically standardized

## Slide 24: Nitrification
Water quality standards
TAN – Total Ammonia Nitrogen (NH3/NH4+)
  <3.0 mg/L for warm-water fish <1.0 mg/L for cold-water fish
  Nitrosomonas bacteria
Nitrite (NO2)
  <1.0 mg/L unless soft water (should be <0.1 mg/L)
  Nitrobacter bacteria
NH4+ + 1.5O2 NO2- +2H+ + H2O
NH4+ + 2O2 NO3- +2H+ + H2O
NO2- + 0.5O2 NO3-
Important note: For every gram of NH4+ converted, 4.57 g of O2 is used

## Slide 25: Sizing Biofilter for Nitrogen (TAN removal)
TAN = (0.092 *% Protein in feed) x Feed per day (g)
Estimated removal is 0.45 g TAN/m2 day

## Slide 26: Problem: Sizing Filter
What size MBBR biofilter do you need for growing 100 lb. of fish?
  Assume 30% protein feed; 2% daily feeding rate, Biomedia Effective Surface Area: 250 m2/m3
  Also assume areal tan removal (ATR) is 0.45 g TAN/m2 day
  Step 1)
  (2% of 100 lb. = 2 lb. ~1 kg)
  = 0.0276 ~ 0.03 kg TAN/day
  Step 2) 30 g TAN / 0.45 g TAN/ m2 day = 66.7 m2 of surface area required
  Step 3) 66.7 m2 / 250 m2/m3 = 0.27 m3 of biomedia needed
  Step 4) 0.27 m3 / 50% of container volume = 0.54 m3 (required volume)
  *Biofilter container should be ~140 gallons

## Slide 27: Filtration Review
Solids Filters
  Remove TSS
  Goal should be removal of >70% of solids if commercial system
    especially large and coarse solids
  Help prevent biofilter overload and maintain water quality
Biofilters
  Convert ammonia (excreted by fish) to nitrate
  Rely on adequate oxygen (aeration) and adequate surface area